## Slide 2: Why should organizations care about hurricane risk?
Significant portions of the United States are at risk for the effects of tropical storms and hurricanes. It is important that organizations throughout the country, including associations, businesses, and community groups, understand the risks and potential impacts and prepare accordingly.
The Ready Business Program for Hurricane and the Preparedness and Mitigation Project Plan allow users to take action to protect employees, protect customers, and help ensure business continuity.
Source: “Major Hurricane History.” Map. National Weather Service.
NATURAL DISASTER IMPACT |  | 
IMMEDIATE 40% OF SMALL BUSINESSES WON’T REOPEN | ONE YEAR LATER 25% MORE SMALL BUSINESSES WILL CLOSE | THREE YEARS LATER 75% OF BUSINESSES WITHOUT A CONTINUITY PLAN WILL FAIL

## Slide 3: Table of Contents
INTRODUCTION | 4
Program Overview | 7
Benefits | 8
1 ¦ IDENTIFY YOUR RISK | 10
Back-to-Business Self-Assessment | 11
Assess Your Readiness | 12
2 ¦ DEVELOP A PLAN | 14
STAFF/SURROUNDINGS/SPACE/SYSTEMS/STRUCTURE/SERVICE | 16
STAFF | 17
SURROUNDINGS | 19
SPACE | 20
SYSTEMS | 21
STRUCTURE | 22
SERVICE | 25
Quick Reference Guide | 26
3 ¦ TAKE ACTION | 43
Applications | 45
Feedback | 53
Valuable Websites | 54
APPENDIX A ¦ Acronyms and Glossary | 55
APPENDIX B ¦ Acronyms and Glossary | 59

## Slide 4: INTRODUCTION

## Slide 5: Introduction
Should your organization be concerned about tropical storms and hurricanes? In many instances, yes. Many parts of the United States, including Atlantic and Gulf of Mexico coastal areas, Hawaii, parts of the Southwest, Puerto Rico, the Pacific Coast, and the U.S. Virgin Islands and territories in the Pacific may be directly affected by heavy rains, strong winds, wind-driven rain, coastal and inland floods, tornadoes, and coastal storm surges resulting from tropical storms and hurricanes.
The National Hurricane Center reports the greatest threat to life and property along the coasts are storm surge and large waves caused by hurricanes. In addition, heavy rainfall can result in extensive flooding, including inland flooding. According to the National Oceanic and Atmospheric Administration, inland flooding accounts for more than 50 percent of hurricane-related deaths each year. Furthermore hurricane-force winds and windborne debris from tropical storms and hurricanes can destroy buildings and mobile homes and pose a major risk to people and property.
If your organization is vulnerable to hurricanes, it is important that you understand your risk, develop a preparedness and mitigation plan, and take action. Doing so will not only ensure the safety of employees and customers, but it will help you remain in business after disasters, such as tropical storms and hurricanes, strike. Maintaining business continuity is important. When you are able to continue operations after a disaster, you also improve your community’s ability to recover.
 | Identify Your Risk
 | Develop a Plan
 | Take Action
THE READY BUSINESS PROGRAM MOVES ORGANIZATIONAL LEADERS THROUGH A STEP-BY-STEP PROCESS TO:

## Slide 6: Introduction (continued)
Following these steps in the Ready Business Program as a part of your overall business continuity planning will help protect assets (people, property, operations); sustain the capability to provide goods and services to customers and/or supply chain; maintain cash flow; preserve competitive advantage and reputation; and provide the ability to meet legal, regulatory, financial, and contractual obligations.
Nonprofit organizations can also benefit from the Ready Business Program as business continuity will protect staff, clients, and property while allowing operations to continue.
The Small Business Administration (SBA) estimates that 75 percent of businesses without continuity planning will fail within three years of a disaster. The Ready Business Program offers information to complete continuity planning, including resources from the Federal Emergency Management Agency (FEMA) Business Continuity Plan website.
Once completed, the Ready Business Program will provide you with the tools to plan, take action, and become a Ready Business by addressing preparedness and mitigation for your STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE. And you will also have the opportunity to apply for recognition as a member of the Ready Business Community.

## Slide 7: Introduction: Program Overview
Organizations can achieve six levels for recognition through the Ready Business Program. The levels include STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE. The first five levels can be achieved either independently or as a group. The SERVICE level can be achieved by completing requirements for STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE.
STAFF includes planning and preparedness activities for the protection of your staff.
SURROUNDINGS includes those elements that potentially pose a threat during an event, such as fences, flagpoles, and trees.
SPACE includes the contents of your workspace, such as inventory, filing cabinets, shelving, and other furniture.
SYSTEMS includes utility systems that support the operation of the building and are generally located on the roof.
STRUCTURE includes architectural and structural elements of the building, especially construction types that may be vulnerable to damage or failure during an event.
SERVICE includes the opportunities for your organization to engage and serve the community following an event. You may only qualify for SERVICE to others after you have prepared your own organization first.
It is important to remember that injury, damage, concurrent damage, cascading disasters like fire following the event, business interruption, or even increased repair or recovery costs can come from failure to prepare or mitigate. As a result, the first step in the Ready Business Program is to complete a Back-to-Business Self-Assessment to identify vulnerabilities from any source.
The Ready Business Program is intended to recognize and reward organizations who complete preparedness and mitigation actions to protect employees, customers, and continuity. You can get started today by following the steps provided.
For more information or assistance, contact info@flash.org or (877) 221-7233.

## Slide 8: Benefits of participating in the program and achieving recognition include
Peace of mind that your organization is prepared not only for hurricanes, but for other business interruptions and natural disasters.
Ready Business window cling to announce to your customers or clients and employees that you have taken steps to prepare your STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and are prepared to be of SERVICE after an event.
Ready Business recognition certificate.
Ready Business web badge to display on your organization’s website.
Organization Listing on Ready Business website.
Sample news release to announce your organization’s participation in the Ready Business Program and tips for media placement.

## Slide 9: Introduction: Ready Business Program
IDENTIFY YOUR RISK
Complete the Back-to-Business Self-Assessment to determine the specific areas your organization needs to address to prepare, mitigate risk, and return to operation following a disaster.
DEVELOP A PLAN
Based on the information in the Back-to-Business Self-Assessment, complete the Ready Business Preparedness and Mitigation Project Plan for STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE to identify preparedness and mitigation actions needed to ensure safety and business continuity. (Note: Completing this plan is a critical first step toward recognition as a Ready Business.)
Review the Quick Reference Guide to determine which preparedness and mitigation actions to take based on the potential impacts to your organization.
If you need assistance with Ready Business planning, contact your local emergency management office to discuss local hazards, identify local best practices in disaster safety and resilience, or connect with other Ready Businesses in your community.
TAKE ACTION
Now that you’ve created your Preparedness and Mitigation Project Plan, make sure the building owner approves it if you are leasing or renting your building. (Note: Be sure to check with your local building department to secure required permits prior to performing any retrofitting or other mitigation activity.)
Perform preparedness and mitigation activities as prioritized in the Preparedness and Mitigation Project Plan. Document your actions as instructed in the applications for STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE with signatures, photographs, receipts, or letters from an organization manager, engineer, or design professional, as applicable.
Complete the application at the end of the program for recognition as a Ready Business.
After you have completed these steps, you will be eligible to become a member of the Ready Business Community, and will enjoy the peace of mind of knowing you have done your part to promote safety, mitigate potential loss, and protect your organization.
1
2
3

## Slide 10: IDENTIFY YOUR RISK

## Slide 11: Identify Your Risk: Back-to-Business Self-Assessment
PLANNING SCENARIO
On August 1 of this year, a hurricane strikes your community and damages both the structure and the contents in the building where your organization operates. Due to damage, your building has been ‘yellow tagged’ during a rapid assessment by the building department and is closed. A more thorough assessment of your building damage is needed to determine if your structure is safe, or can be made safe, prior to reopening.
Due to the number of buildings damaged in your community, your building’s detailed damage assessment will take place three days after the event. You should assume you will not be able to access your facilities for at least three days.
Depending on your type of organization, expect that either 50 percent of your inventory (product) is unsellable, or that 50 percent of your computers or other equipment was damaged during the event (choose whichever creates the greater impact on your organization). Assume that all utilities are interrupted.
Further, you should project that the disruptions will continue for one additional day. The assessment will show that the damage is repairable to the structure, so now you will need to address staff, contents, cleanup, repairs, and replacement.
Based on this scenario, complete the 13 questions on the following pages to identify your risk.
1

## Slide 12: Identify Your Risk: Back-to-Business Self-Assessment
ASSESS YOUR READINESS
Based on the planning scenario, complete the 13 questions below to highlight areas that your Business Continuity and Preparedness and Mitigation Plan should address.
IMPACTS ON YOUR ORGANIZATION |  | RESOURCES THAT CAN HELP MINIMIZE DAMAGE, DISRUPTIONS, AND INJURIES
SYSTEMS/STRUCTURE |  | 
Can your organization operate without any of the following: computers, copier, fax machine, files, inventory, or special equipment (e.g., x-ray equipment, cash register, credit card readers)? | Yes No | Ready Business Program – SYSTEMS
Can your organization operate without any of the following: gas, power, water, internet, or telecommunications? | Yes No | Ready Business Program – SYSTEMS
Can you still operate your organization without access to the damaged building(s)? | Yes No | Ready Business Program – STRUCTURE
STAFF/CUSTOMERS/VENDORS/SUPPLIERS (PEOPLE) |  | 
Can you meet payroll if your business income is interrupted? If yes, estimate how long? | Yes No | Business Continuity Plan – PEOPLE
Are your employees able to commute to work? | Yes No | Business Continuity Plan – PEOPLE
IMPACT ON YOUR ORGANIZATION |  | 
Is your organization easily accessible to the public, your customers, and employees (e.g., parking)? | Yes No | Business Continuity Plan – PEOPLE
Are you communicating status with employees, key customers, vendors, and suppliers throughout your recovery? | Yes No | Business Continuity Plan – PEOPLE

## Slide 13: Identify Your Risk: Back-to-Business Self-Assessment (continued)
IMPACTS ON YOUR ORGANIZATION |  | RESOURCES THAT CAN HELP MINIMIZE DAMAGE, DISRUPTIONS, AND INJURIES
OPERATIONS |  | 
Can your organization operate without access to the damaged buildings? | Yes No | Business Continuity Plan – OPERATIONS
Have you set priorities on what operations your organization needs to recover 1st, 2nd, 3rd, etc.? | Yes No | Business Continuity Plan – OPERATIONS
Are your suppliers up and running or do you have sufficient parts/supplies on hand to continue without resupply? | Yes No | Business Continuity Plan – OPERATIONS
Are you able to ship your product or provide services to your customers based on your current impacts, understanding that the demand for these products or services may drastically change? | Yes No | Business Continuity Plan – OPERATIONS
Will you still have all your customers/clients after the disaster? | Yes No | Business Continuity Plan – OPERATIONS
OVERALL OPERATIONS |  | 
Can your organization survive losses if it is closed and/or inaccessible for 3 to 7 days? | Yes No | Ready Business Program & Business Continuity Plan
For each question, 1-13, that you answered ‘No’, address the specific issue in the Ready Business Preparedness and Mitigation Project Plan, or in your Business Continuity Plan. Use the Ready Business Program resources to help determine the potential for damage to buildings and contents as well as how you will reduce the damage to buildings and contents if it occurs. Resources are incorporated throughout this toolkit and a comprehensive list can be found on pages 59-62. |  | 

## Slide 14: DEVELOP A PLAN

## Slide 15: Develop A Plan
Based on the information in the completed Back-to-Business Self-Assessment, create a Ready Business Preparedness and Mitigation Project Plan for your STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE to identify critical preparedness and mitigation actions needed to ensure safety and business continuity. Completing this plan will bring you one step closer to recognition as a Ready Business.
Review the Quick Reference Guide to determine which preparedness and mitigation actions to take based on the potential impacts to your organization.
If you need assistance with Ready Business planning, contact your local emergency management office to discuss local hazards, identify local best practices in disaster safety and resilience, or connect with other Ready Businesses in your community.
2

## Slide 16: Develop A Plan
STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, AND SERVICE
After you have identified the potential hurricane risks and determined the possible impacts on your organization, create a Preparedness and Mitigation Project Plan and decide which solutions you will use to reduce risks. The Preparedness and Mitigation Project Plan will support the business continuity planning and readiness process and bring you one step closer to recognition as a Ready Business.
READY BUSINESS PREPAREDNESS AND MITIGATION PROJECT PLAN
Organization:
Project Lead:
Name:
Title/Department
Address:
Phone Number:
Email:
Executive Summary:
Background: (Provide a summary description of risk to include priorities)
Goals and Objectives:

## Slide 17: Develop A Plan: STAFF
PREPAREDNESS ACTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Develop Business Continuity and Crisis Communications Plans |  |  | 
Conduct an Employee Awareness Campaign |  |  | 
Develop an Employee Training Program |  |  | 
Conduct an Employee Training Session |  |  | 
Conduct a Hurricane Drill |  |  | 
Review Insurance Coverage (including Flood Insurance)/Create Inventory (Note: See call out box on page 18 regarding special information on flood insurance.) |  |  | 
ADDITIONAL ACTION: Develop an Employee Shelter/Evacuation Plan and Include an Emergency Supply Kit |  |  | 
ADDITIONAL ACTION: Purchase a NOAA Weather Radio for Monitoring During an Event/Download a Mobile Alerting App |  |  | 
1
2
3
4
5
Below is a list of key preparedness measures your organization can complete to ensure your staff is prepared to handle a hurricane; however, the list is not all-inclusive. In addition, even if you are required to evacuate, being prepared allows you to stay in contact with your staff and provides a sense of comfort that your organization will be able to reopen after the disaster. For additional guidance on preparedness measures, please see the Quick Reference Guide: STAFF in this program.
By performing steps one through six, organizations will be eligible for recognition as a Ready Business – STAFF. The Additional Actions are recommended, but not required, for recognition.
6

## Slide 18: Develop A Plan: STAFF
FLOOD INSURANCE IS CRITICAL FOR BUSINESSES AND EMPLOYEES ALIKE
Did you know that homeowners insurance doesn’t cover flood? The National Flood Insurance Program (NFIP) was developed to help provide a means for property owners to financially protect themselves. The NFIP offers flood insurance to homeowners, renters, and business owners if their community participates in the NFIP. Participating communities agree to adopt and enforce ordinances that meet or exceed FEMA requirements to reduce the risk of flooding. The average flood insurance policy costs about $700 per year. To learn more about the NFIP and flood insurance in your area, visit FloodSmart.

## Slide 19: Develop A Plan: SURROUNDINGS
SURROUNDINGS RISKS | MITIGATION SOLUTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Signs | Reinforce signs to withstand expected wind pressures or remove prior to event. |  |  | 
Flagpoles | Secure flagpole(s) to withstand expected wind pressures or remove prior to event. |  |  | 
Landscaping/Trees | Consult a professional landscaper and develop a plan for hurricane-resilient landscaping. |  |  | 
Fences | Ensure fencing is installed securely. |  |  | 
Floodwalls and Levees | Consult with a floodplain manager or professional engineer regarding land use or code restrictions/ requirements in your area. If elevating the structure or performing floodproofing techniques is not feasible, then consider designing floodwalls or levees on the property to attempt to repel floodwaters. |  |  | 
Below is a list of nonstructural hurricane mitigation activities that can be completed by a professional landscaper/tradesman or professional engineer; however, the list is not all-inclusive. For additional guidance on nonstructural risks, please see the Quick Reference Guide: SURROUNDINGS in this program.
By performing all applicable activities, organizations will be eligible for recognition as a Ready Business – SURROUNDINGS.

## Slide 20: Develop A Plan: SPACE
NONSTRUCTURAL RISKS | MITIGATION SOLUTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Contents | Determine and relocate your critical contents at least one foot above the Base Flood Elevation (BFE) or the Design Flood Elevation (DFE), whichever is higher. |  |  | 
Chemicals | Establish a method for safeguarding chemicals in your Preparedness and Mitigation Project Plan. |  |  | 
Below is a list of nonstructural mitigation activities that can be completed by someone with common tools and readily available materials; however, the list is not all-inclusive. For additional guidance on mitigating these nonstructural risks, please see the Quick Reference Guide: SPACE in this program.
By performing all mitigation activities, organizations will be eligible for recognition as a Ready Business – SPACE.

## Slide 21: Develop A Plan: SYSTEMS
SYSTEMS RISKS | MITIGATION SOLUTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Mechanical Systems | Consult a professional engineer to ensure all systems and connections are designed to resist the expected wind load and uplift and to develop solutions for protecting vital systems through elevation, anchoring, or other approved means. Protect drainage systems with backflow valves. Consult a professional plumber for proper installation of these devices. |  |  | 
Fuel Tanks/Systems |  |  |  | 
Electrical Systems |  |  |  | 
Communications Equipment |  |  |  | 
Lightning Protection Systems |  |  |  | 
Utility Connections |  |  |  | 
Antennas |  |  |  | 
Other Rooftop Structures |  |  |  | 
Sewer and Water Management Systems |  |  |  | 
Potable Water Systems |  |  |  | 
Below is a list of nonstructural mitigation activities that may require a professional engineer to identify and evaluate appropriate mitigation steps; however, the list is not all-inclusive. For additional guidance on nonstructural risks, please see the Quick Reference Guide: SYSTEMS in this program.
By performing all retrofit items, organizations will be eligible for recognition as a Ready Business – SYSTEMS.

## Slide 22: Develop A Plan: STRUCTURE
STRUCTURAL RISKS | MITIGATION SOLUTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Continuous Load Path – Foundation | Consult a professional engineer to evaluate elevation and continuous load path. |  |  | 
Roof Systems | Consult a professional engineer and design the roof to withstand the expected wind loads, uplift, and water intrusion. Create a continuous load path, consider the integrity of roof coverings and decking, and install flashing to minimize water intrusion through vents or other openings. |  |  | 
Skylights | Upgrade to pressure-related, impact-resistant skylights. |  |  | 
Gable-End Bracing | Consult a professional to properly brace the gable-end walls. |  |  | 
Soffits | Consult a professional and ensure that soffits are properly supported. |  |  | 
Assessing structural and complex nonstructural risk requires the services of a professional engineer or other design professional to accurately evaluate and design reasonable mitigation measures. Below is a list of mitigation solutions; however, the list is not all-inclusive. For additional guidance on structural risks, please see the Quick Reference Guide: STRUCTURE in this program.
By performing a minimum of one retrofit item on this list, organizations will be eligible for recognition as a Ready Business – STRUCTURE.

## Slide 23: Develop A Plan: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Gutters and Downspouts | Install systems that are noncombustible and designed for wind speed and uplift resistance. |  |  | 
Wall Systems | Consult a professional engineer and design the wall system to withstand the expected wind loads, pressure, and water intrusion. Create a continuous load path, ensure the integrity of wall coverings and sheathing, and install adequate flashing to minimize water intrusion. |  |  | 
Openings • Garage/Rolling Doors • Windows • Exterior Doors | Install pressure-rated, impact-resistant exterior doors, windows, and garage/rolling doors. Install storm shutters or other tested and approved protection on any unprotected openings. |  |  | 
Canopies, Awnings, and Carports | Add supports to increase resistance to wind loads and uplift. |  |  | 
Safe Room or Shelter | Install a safe room or shelter that meets FEMA Guidelines or ICC/NSSA 500 Standards. Note: If the structure is located in a flood zone, safe rooms and shelters are not recommended. |  |  | 

## Slide 24: Develop A Plan: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Best Available Refuge Area (BARA) | Consult a professional engineer to strengthen the BARA if a shelter is not installed. Note: Do not plan to shelter-in-place if your structure is in a flood or storm surge evacuation zone. |  |  | 
Elevation | Consult a professional engineer to evaluate elevation of the structure so that the top of the lowest floor is at or above the BFE or DFE, whichever is higher. |  |  | 
Wet Floodproofing | Consult a professional engineer to evaluate options for wet floodproofing the structure. |  |  | 
Dry Floodproofing | Consult a professional engineer to evaluate options for dry floodproofing the structure. |  |  | 

## Slide 25: Develop A Plan: SERVICE
SERVICE ACTION | ASSIGNED TO | BUDGET | COMPLETION DATE
Contact your Local Emergency Management Office |  |  | 
Identify Ways to Engage and Participate in Your Community |  |  | 
If your organization is open after the disaster, you could become a distributor or storage warehouse for Disaster Relief Kits. Providing a place for the supplies to be stored locally allows volunteer organizations to readily distribute them throughout affected areas. | Does your organization have electricity after the disaster? If so, you may want to become a volunteer charging station. Provide a safe, secure place for emergency responders, volunteers, and community members to charge their cell phones or battery-powered tools. | Does your organization have the capability to prepare or serve meals? Providing a sanitary kitchen for emergency responders, volunteers, or community members to prepare or receive meals following a disaster is essential for rebuilding the community. | Not sure how your organization can directly contribute after the disaster? Volunteer. Contact your Local Emergency Manager and determine where volunteer opportunities exist in the community. You could prepare meals, sort debris, or even work at a local office of a volunteer organization. For additional ideas, visit National Voluntary Organizations Active in Disaster.
Can your organization provide community service to others following a disaster? Identify and build local relationships to create a SERVICE component in your Business Continuity Plan. For additional guidance on the SERVICE component, please see the Quick Reference Guide: SERVICE in this program.
By performing all applicable preparedness activities in STAFF and mitigation actions in SURROUNDINGS, SPACE, SYSTEMS, and STRUCTURE, organizations will be eligible for recognition as a Ready Business – SERVICE.

## Slide 26: Quick Reference Guide: STAFF
PREPAREDNESS ACTION | PREPAREDNESS SOLUTIONS | PREPAREDNESS RESOURCES
STEP 1: Develop Business Continuity and Crisis Communications Plans | Create a Business Continuity Plan that includes strategies for storing critical business documents and data. | Business Continuity Plan
 | Consult the Disaster Resistant Business Toolkit. | Disaster Resistant Business (DRB) Toolkit
 | Assign a Business Continuity Team Leader responsible for implementing the Business Continuity Plan to bring your organization back to business after an event. | Business Continuity Plan
 | Create a Crisis Communications Plan that includes internal and external communication protocols for before, during, and after a disaster. | Crisis Communications

## Slide 27: Quick Reference Guide: STAFF (continued)
PREPAREDNESS ACTION | PREPAREDNESS SOLUTIONS | PREPAREDNESS RESOURCES
STEP 2: Conduct an Employee Awareness Campaign | Conduct an employee awareness campaign to educate staff on disaster safety. The awareness campaign should include educating staff on the safest response before, during, and after a hurricane, including definitions of National Hurricane Center (NHC) terms, e.g., tropical storm/hurricane watch vs. warning. Address shelter locations, emergency communication plans and policies, when to evacuate (when advised), seeking high ground for flash flooding, and avoiding entering flood waters. The campaign should also provide guidance on critical actions after a hurricane event. Advise employees to learn their BFE by visiting the online FEMA Flood Map Service Center, contacting their insurance company, or calling their local floodplain management department. Reference How to Prepare for a Hurricane for additional content. | FEMA. How to Prepare for a Hurricane. America’s PrepareAthon! FEMA Flood Map Service Center

## Slide 28: Quick Reference Guide: STAFF (continued)
PREPAREDNESS ACTION | PREPAREDNESS SOLUTIONS | PREPAREDNESS RESOURCES
STEP 3: Develop an Employee Training Session | Develop a training program that provides activities for employee engagement before, during, and after a hurricane. Your training can be incorporated into established campaigns like National Preparedness Month and should focus on disaster preparedness and safety. Drills or exercises should be incorporated into the program. Include Turn Around, Don’t Drown! into your messaging. | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! Turn Around, Don’t Drown!
STEP 4: Conduct an Employee Training Session | Hold a preparedness discussion with your staff. Discuss what you have done to prepare for disasters, review your Business Continuity Plan, review your Crisis Communication Plan, and share awareness campaign key messages. Use the Prepare Your Organization for a Hurricane Playbook to facilitate this discussion and engage your employees. The discussion should: Educate the employees about your business continuity and crisis communications plans; Include basic first aid and CPR training; and, Describe evacuation and shelter plans. | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon!

## Slide 29: Quick Reference Guide: STAFF (continued)
PREPAREDNESS ACTION | PREPAREDNESS SOLUTIONS | PREPAREDNESS RESOURCES
STEP 5: Conduct a Hurricane Drill | Conduct your disaster drill, but before you begin, contact your local emergency manager for additional ideas and to offer them a way to participate. | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! Turn Around, Don’t Drown!
STEP 6: Review Insurance Coverage (Including Flood Insurance)/ Create Inventory | Meet with your insurance agent annually to review your insurance, especially property coverage limits, deductibles, and coinsurance requirements. Maintain a current photo or video inventory of your premises, equipment, inventory, supplies, etc. | Insurance Coverage Discussion Form
ADDITIONAL ACTION: Develop an Employee Shelter/ Evacuation Plan and Include an Emergency Supply Kit | Develop an employee shelter/ evacuation plan to include an emergency kit with supplies you may need before, during, and/or after the disaster. | Emergency Supply List

## Slide 30: Quick Reference Guide: STAFF (continued)
PREPAREDNESS ACTION | PREPAREDNESS SOLUTIONS | PREPAREDNESS RESOURCES
ADDITIONAL ACTION: Purchase a NOAA Weather Radio for Monitoring During an Event/ Download a Mobile Alerting App | Purchase a NOAA Weather Radio with single area message encoding (SAME) and download a severe weather alerts app for your mobile device. You may also sign up to receive emergency notifications from your local emergency services. Download Be Smart. Take Part. Know Your Alerts and Warnings for a summary of available notifications. Designate a Team Leader and assign them to monitor your NOAA Weather Radio during an event. Listen and heed instructions given by local emergency management officials. Have backup batteries and chargers. | NOAA Weather Radio All Hazards Be Smart. Take Part. Know Your Alerts and Warnings

## Slide 31: Quick Reference Guide: STAFF (continued)
RESOURCES:
FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon!
FEMA. How to Prepare for a Hurricane. America’s PrepareAthon!

## Slide 32: Quick Reference Guide: SURROUNDINGS
SURROUNDINGS RISKS | MITIGATION SOLUTION | REFERENCES
Signs | Consult a professional landscaper, and develop a plan for your surroundings that mitigates against damage from hurricanes by removing dead branches and other potential projectiles or falling trees. | Remove Trees and Potential Windborne Missiles: Protecting Your Property from High Winds
Flagpoles |  | 
Landscaping/Trees |  | 
Fences |  | 
Floodwalls and Levees | Consult with a floodplain manager or professional engineer regarding land use or code restrictions/requirements in your area. If elevating the structure or performing floodproofing techniques is not feasible, then consider designing floodwalls or levees on the property to attempt to repel floodwaters. | FEMA P-936, Floodproofing NonResidential Buildings FEMA P-259, Engineering Principles and Practices for Retrofitting Flood-Prone Residential Structures

## Slide 33: Quick Reference Guide: SPACE
SPACE RISKS | MITIGATION SOLUTION | REFERENCES
Contents | Determine and relocate your critical contents at least one foot above the BFE or the DFE, whichever is higher, | FEMA P-936, Floodproofing Non-Residential Buildings
Chemicals | Establish a method for safeguarding chemicals in your Preparedness and Mitigation Project Plan. | Emergency Response Plan

## Slide 34: Quick Reference Guide: SYSTEMS
SYSTEMS RISKS | MITIGATION SOLUTION | REFERENCES
Mechanical Systems | Consult a professional engineer to evaluate and design structural connections to resist the expected wind loads and provide uplift resistance. Additionally, consult a professional to evaluate and design for the following flood mitigation techniques: Elevate service equipment at least 12-inches above BFE. Use platforms or pedestals for equipment installed on the ground. Relocate equipment to an existing location above the BFE. Protect the equipment in place with floodwalls, shields, or anchors and tie-downs. Protect drainage systems with backflow valves. Consult a professional plumber for proper installation of these devices. | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds FEMA P-259, Engineering Principles and Practices for Retrofitting FloodProne Residential Structures FEMA P-936, Floodproofing Non-Residential Buildings
Fuel Tanks/Systems |  | 
Electrical Systems |  | 
Communications Systems |  | 
Lightning Protection Systems |  | 
Utility Connections |  | 
Antenna |  | 
Other Rooftop Structures |  | 
Sewer and Water Management Systems |  | 
Potable Water Systems |  | 

## Slide 35: Quick Reference Guide: STRUCTURE
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Continuous Load Path – Foundation | Consult a professional engineer to evaluate elevation and continuous load path. The entire structure can be bolted to its foundation using anchor bolts along the foundation sill. | FEMA. How to Prepare for a Hurricane. America’s PrepareAthon!
Roof Systems | Consult a professional engineer to design the roof to withstand the expected wind loads, provide uplift resistance, and prevent water intrusion. Consider the many features that define a roof, including slope, structure, covering, and attachments, and address the roof as a system. Ensure that the following design/ mitigation measures are included: Roof-to-Wall Connections Roof Structure Roof Decking/Sealant Roof Covering Roof Flashing Vents | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds Secure Built-Up and Single-Ply Roofs: Protecting Your Property from High Winds
The International Code Council’s International Building Code (IBC) addresses construction methods for most commercial structures as well as residential structures that are not covered by the International Residential Code. The IBC contains both prescriptive and engineered provisions, and applies to the many different types of commercial structures.
It is important to note that the recommendations in this document are general and are intended to highlight areas of a structure that could be strengthened against hurricanes. However, the recommendations cannot account for all of the different building types and variables in the IBC. As a result, a licensed professional is necessary to identify and perform mitigation activity appropriate for your organization.

## Slide 36: Quick Reference Guide: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Skylights | Upgrade to pressure-rated, impact-resistant skylights. | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds
Gable-End Bracing | Hire a professional to brace any gable-end walls taller than 4 feet so that loads on the gable-end walls are distributed over multiple roof trusses or rafters. | FEMA P-499, Home Builder’s Guide to Coastal Construction
Soffits | Proper attachment is the most common cause of soffit failures. This can be addressed by installing wood backing or supports as an attachment point for soffits. If it is not possible to install wood supports, the soffit should be secured at 12-inch intervals on each side to limit flexing during high-wind events. | FEMA P-499, Home Builder’s Guide to Coastal Construction

## Slide 37: Quick Reference Guide: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Gutters and Downspouts | Install noncombustible systems designed for high-wind speeds that provide uplift resistance. | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds
Wall Systems | Consult a professional engineer to design walls to withstand high-wind loads, provide uplift resistance, and prevent water intrusion. Consider the many features that define a wall, including structure, covering, and openings. Address the wall as a system, ensuring the following design/mitigation measures are included: Wall Structure Wall Sheathing House Wrap Wall Coverings Flashing Around Openings | FEMA P-499, Home Builder’s Guide to Coastal Construction Secure Metal Siding and Metal Roofs: Protecting Your Property from High Winds Maintain EIFS Walls: Protecting Your Property from High Winds

## Slide 38: Quick Reference Guide: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Openings Garage/Rolling Doors Windows Exterior Doors | Install pressure-rated, impact-resistant garage doors or brace existing doors with assemblies designed to increase pressure ratings. Install pressure-rated, impact-resistant windows, or protect with tested and approved opening protection. If these options are not available, as a temporary measure use 5/8-inch or greater plywood, cut to fit and ready to install, and do not use tape, as it does not protect against broken glass. Install pressure-rated, impact-resistant exterior doors. Ensure flashing and weather stripping around the windows and doors is designed/installed to protect against water intrusion from wind-driven rain. | Reinforce or Replace Garage Doors: Protecting Your Property from High Winds Protect Windows and Doors with Covers: Protecting Your Property from High Winds FEMA P-499, Home Builder’s Guide to Coastal Construction FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds

## Slide 39: Quick Reference Guide: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Canopies, Awnings, and Carports | Add metal connectors to meet or exceed expected wind loads. For the carport, consider placing connectors: Between supporting roof members and horizontal beams; At each beam-to-column connection; and At each column-to-foundation connection. | FEMA P-804, Wind Retrofit Guide for Residential Buildings
Safe Room or Shelter | Install a safe room or shelter that is constructed using FEMA guidance or that meets ICC/NSSA 500 standards in an area safe from flooding. Reference FEMA P-361 and Quick Guide Flood Hazard Elevation and Siting Criteria for Community Safe Rooms for additional information about flood elevation and siting criteria for community safe rooms. Note: If the structure is located in a flood zone, safe rooms and shelters are not recommended. | FEMA P-361, Safe Rooms for Tornadoes and Hurricanes: Guidance for Community and Residential Safe Rooms FEMA P-320, Taking Shelter from the Storm: Building a Safe Room for Your Home or Small Business ICC/NSSA 500-2014: Standard for the Design and Construction of Storm Shelters

## Slide 40: Quick Reference Guide: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Safe Room or Shelter |  | Quick Guide Flood Hazard Elevation and Siting Criteria for Community Safe Rooms
Best Available Refuge Area (BARA) | Consult a professional engineer to strengthen your BARA if a shelter is not installed. Note: Do not plan to shelter-in-place if your structure is in a flood or storm surge evacuation zone. | FEMA P-431, Tornado Protection: Selecting Refuge Areas in Buildings
Elevation | Consult a professional engineer to evaluate elevation of the structure so that the top of the lowest floor is at or above the BFE or DFE, whichever is higher. | FEMA P-550, Recommended Residential Construction for Coastal Areas: Building on Strong and Safe Foundations FEMA P-312, Homeowner’s Guide to Retrofitting
Wet Floodproofing | Wet floodproofing is a technique that allows flood waters to enter the structure. Consult a professional engineer to evaluate options for wet floodproofing the structure. Consider the following items when wet floodproofing: All materials used should be resistant to damage from flood waters. Wet floodproofing does not protect the structure from flowing water, erosion, scour, debris or damage to contents. Post-flood clean-up should be considered before using wet floodproofing techniques. | FEMA P-936, Floodproofing Non-Residential Buildings FEMA P-259, Engineering Principles and Practices for Retrofitting FloodProne Residential Structures

## Slide 41: Quick Reference Guide: STRUCTURE (continued)
STRUCTURAL RISKS | MITIGATION SOLUTION | REFERENCES
Wet Floodproofing | Installation of properly sized and placed wall openings, below the expected flood level. By allowing water to enter the structure, you may cause a secondary issue with protection of systems. Reference the SYSTEMS section to mitigate these items. | 
Dry Floodproofing | Dry floodproofing is a technique that prevents the entry of water into the structure. Dry floodproofing should only be considered in instances where the flood waters are expected to last a short duration and a depth of less than three feet. Because the walls are exposed to floodwaters and the pressures they exert, dry floodproofing is recommended only for structures with walls constructed of flood-resistant materials and depths are low. Consult a professional engineer to evaluate options for dry floodproofing the structure. Consider the following items when dry floodproofing: All exterior walls of the structure must be sealed and possibly reinforced. All openings below BFE must be permanently sealed or have enhanced flood shields installed. Protected from seepage. Anchoring of structure to resist floatation and lateral movement. Selecting and designing proper drainage systems to eliminate excess hydrostatic loads. Design watertight core areas to protect vital systems if dry floodproofing the entire structure is not possible. | FEMA P-936, Floodproofing NonResidential Buildings FEMA P-259, Engineering Principles and Practices for Retrofitting FloodProne Residential Structures

## Slide 42: Quick Reference Guide: SERVICE
SERVICE ACTION | POTENTIAL MITIGATION SOLUTION | REFERENCES
Contact your Local Emergency Management Office | Contact your local emergency management office to identify emergency management personnel and resources in your area. | Emergency Management Agencies
 | Contact your local emergency management office during your disaster planning to learn how you may provide service(s) before and after a disaster strikes. Include this information in your Business Continuity Plan. | 
Identify Ways to Engage and Participate in your Community | In addition to preparing your organization, it is important to understand your local and tribal community emergency operations plans and to work with other organizations in your community or tribe. Opportunities to participate in whole community planning include the following: Learn about public-private partnerships. Participate in local or tribal organizations that make your community a safer and more prepared place to live and do business, such as your local Citizen Corps Council, hazard mitigation planning team, or local and tribal Community Emergency Response Team (CERT). Citizen Corps Council includes representatives from all sectors of the community. This whole community membership helps to ensure the community perspective is reflected in local emergency management practices. | FEMA. Prepare Your Organization for a Hurricane Playbook.America’s PrepareAthon!

## Slide 43: TAKE ACTION

## Slide 44: Take Action
Make sure that your Preparedness and Mitigation Project Plan is approved by the building owner if you are leasing or renting your building. Always check with your local building department to secure required permits prior to performing any retrofitting or other mitigation activity.
Perform preparedness and mitigation activities as prioritized in the Preparedness and Mitigation Project Plan. Document your preparedness and mitigation as instructed in the applications for STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, and SERVICE with signatures, photographs, receipts, or letters from an organization manager, engineer, or design professional.
Complete the following application and submit for recognition as a Ready Business.
3

## Slide 45: Take Action: Ready Business Applications
PLEASE COMPLETE:
Organization Name:
Owner/Manager:
Address:
Phone Number: Fax:
Email:
Organization Website URL:
STAFF, SURROUNDINGS, SPACE, SYSTEMS, STRUCTURE, AND SERVICE APPLICATIONS
Now that you have taken the steps to prepare and mitigate your organization to protect customers and employees, you can gain recognition for your accomplishment by completing the application to join the Ready Business Community.
Once you join, you will receive a Ready Business recognition certificate, window cling, and web badge to let your customers and staff know that you are a Ready Business. In addition, your organization will be added to the list of program participants on the Ready Business website. You will also receive a sample news release that you may use to let your community know that you have taken action to prepare.
READY BUSINESS DESIGNATION LEVEL (Please indicate each level you are applying for): | 
Ready Business – STAFF | Must complete steps one through six for STAFF recognition
Ready Business – SURROUNDINGS | Must complete all applicable SURROUNDINGS mitigation activities for recognition
Ready Business – SPACE | Must complete all applicable SPACE activities for recognition
Ready Business – SYSTEMS | Must complete all applicable SYSTEMS activities for recognition
Ready Business – STRUCTURE | Must complete one of the applicable STRUCTURE activities for recognition
Ready Business – SERVICE | Must complete all applicable SERVICE activities and STAFF, SURROUNDINGS, SPACE, SYSTEMS, and STRUCTURE for recognition
Provide documentation of preparedness actions and mitigation performed on the following pages.

## Slide 46: Take Action: Ready Business – STAFF Application
PREPAREDNESS ACTIONS | ACCOMPLISHED | INITIAL/DATE OF RESPONSIBLE PERSON
Developed Business Continuity and Crisis Communication Plans | Must be completed to receive recognition | 
Conducted an Employee Awareness Campaign | Must be completed to receive recognition | 
Developed an Employee Training Program | Must be completed to receive recognition | 
Conducted an Employee Training Session | Must be completed to receive recognition | 
Conducted a Hurricane Drill | Must be completed to receive recognition | 
Reviewed Insurance Coverage(Including Flood Insurance)/ Created Inventory | Must be completed to receive recognition | 
ADDITIONAL ACTION: Developed an Employee Shelter/Evacuation Plan and Included an Emergency Supply Kit | Yes No Not Applicable | 
ADDITIONAL ACTION: Purchased a NOAA Weather Radio for Monitoring During an Event/Downloaded a Mobile Alerting App | Yes No Not Applicable | 
1
2
3
4
5
6

## Slide 47: Take Action: Ready Business – SURROUNDINGS Application
SURROUNDINGS RISKS | MITIGATION SOLUTION | ACCOMPLISHED | INITIAL/DATE OF PERSON RESPONSIBLE
Signs | Reinforced signs to withstand expected wind pressures or removed prior to event. | Yes No Not Applicable | 
Flagpoles | Secured flagpole(s) to withstand expected wind pressures or removed prior to event. | Yes No Not Applicable | 
Landscaping/Trees | Consulted a professional landscaper and developed a plan for hurricane-resilient landscaping. | Yes No Not Applicable | 
Fences | Ensured fencing is installed securely. | Yes No Not Applicable | 
Floodwalls and Levees | Consulted with a floodplain manager or professional engineer regarding land use or code restrictions/ requirements in your area. If elevating the structure or performing floodproofing techniques is not feasible, then consider designing floodwalls or levees on the property to attempt to repel floodwaters. | Yes No Not Applicable | 

## Slide 48: Take Action: Ready Business – SPACE Application
SPACE RISKS | MITIGATION SOLUTION | ACCOMPLISHED | INITIAL/DATE OF PERSON RESPONSIBLE
Contents | Determined and relocated all critical contents at least one foot above the BFE or DFE, whichever is higher. | Yes No Not Applicable | 
Chemicals | Established a method for safeguarding chemicals in your Preparedness and Mitigation Project Plan. | Yes No Not Applicable | 

## Slide 49: Take Action: Ready Business – SYSTEMS Application
SYSTEMS RISKS | MITIGATION SOLUTION | ACCOMPLISHED | INITIAL/DATE OF PERSON RESPONSIBLE
Mechanical Systems | Consulted a professional engineer to ensure all systems and connections are designed to resist the expected wind load and uplift, and to develop solutions for protecting systems from flooding through elevation, anchoring, or other approved means. Protected drainage systems with backflow valves. Consulted a professional plumber for proper installation of these devices. | Yes No Not Applicable | 
Fuel Tanks/Systems |  | Yes No Not Applicable | 
Electrical Systems |  | Yes No Not Applicable | 
Communications Equipment |  | Yes No Not Applicable | 
Lightning Protection Systems |  | Yes No Not Applicable | 
Utility Connections |  | Yes No Not Applicable | 
Antennas |  | Yes No Not Applicable | 
Other Rooftop Structures |  | Yes No Not Applicable | 
Sewer and Water Management Systems |  | Yes No Not Applicable | 
Potable Water Systems |  | Yes No Not Applicable | 

## Slide 50: Take Action: Ready Business – STRUCTURE Application
STRUCTURAL RISKS | MITIGATION SOLUTION | ACCOMPLISHED | INITIAL/DATE OF PERSON RESPONSIBLE
Continuous Load Path - Foundation | Consulted a professional engineer to evaluate elevation and continuous load path. | Yes No Not Applicable | 
Roof Systems | Consulted a professional engineer and designed the roof to withstand the expected wind loads, uplift, and water intrusion. Created a continuous load path, considered the integrity of roof coverings and decking, and installed flashing to minimize water intrusion through vents or other openings. | Yes No Not Applicable | 
Skylights | Upgraded to pressure-rated, impact-resistant skylights. | Yes No Not Applicable | 
Gable-End Bracing | Consulted a professional engineer to properly brace the gable-end walls. | Yes No Not Applicable | 
Soffits | Consulted a professional to ensure soffits are adequately supported. | Yes No Not Applicable | 
Gutters and Downspouts | Installed noncombustible systems designed for wind speed and uplift resistance. | Yes No Not Applicable | 
Wall Systems | Consulted a professional engineer to ensure the wall can withstand expected wind loads, pressure, and resist water intrusion. Created a continuous load path, ensured the integrity of wall coverings and sheathing, and installed adequate flashing to minimize water intrusion. | Yes No Not Applicable | 

## Slide 51: Take Action: Ready Business – STRUCTURE Application
STRUCTURAL RISKS | MITIGATION SOLUTION | ACCOMPLISHED | INITIAL/DATE OF PERSON RESPONSIBLE
Openings Garage/Rolling Doors Windows Exterior Doors | Installed pressure-rated, impact-resistant exterior doors, windows, and garage/rolling doors. Installed storm shutters or other tested and approved protection on any unprotected openings. | Yes No Not Applicable | 
Canopies, Awnings, and Carports | Added support to withstand wind loads and provide uplift resistance. | Yes No Not Applicable | 
Safe Room or Shelter | Installed a safe room or shelter that meets FEMA Guidelines or ICC/ NSSA 500 Standards. Note: If the structure is located in a flood zone, safe rooms and shelters are not recommended. | Yes No Not Applicable | 
Best Available Refuge Area (BARA) | Consulted a professional engineer to strengthen the BARA if shelter is not installed. Note: Do not plan to shelter-in-place if your structure is in a flood or storm surge evacuation zone. | Yes No Not Applicable | 
Elevation | Consulted a professional engineer to evaluate elevation of the structure so that the top of the lowest floor is at or above the BFE or DFE, whichever is higher. | Yes No Not Applicable | 
Wet Floodproofing | Consulted a professional engineer to evaluate options for wet floodproofing the structure. | Yes No Not Applicable | 
Dry Floodproofing | Consulted a professional engineer to evaluate options for dry floodproofing the structure. | Yes No Not Applicable | 

## Slide 52: Take Action: Ready Business – SERVICE Application
SERVICE ACTION | SERVICE SOLUTION | INITIAL/DATE OF RESPONSIBLE PERSON
Contacted Your Local Emergency Management Office | These activities are written into your Business Continuity Plan. | 
Identified Ways to Engage and Participate in Your Community | These activities are written into your Business Continuity Plan. | 

## Slide 53: Feedback
Tell us about yourself and your organization.
1. TYPE OF ORGANIZATION?
Retail
Professional Office
Restaurant
Service Provider
Nonprofit
Industrial
Daycare Center/School
Other, please list
3. HOW DID YOU HEAR ABOUT THE READY BUSINESS PROGRAM?
FEMA
FLASH
State or local emergency management office
Other, please list
2. HOW MANY PEOPLE DO YOU EMPLOY?
1 - 9
10 - 24
25 - 49
50 - 99
100 - 249
250 - 499
500 or more
4. PLEASE PROVIDE ANY SUGGESTIONS FOR THE READY BUSINESS PROGRAM?
Thank you for your participation in the Ready Business Program. You will receive a response to your application within two to four weeks. For more information or if you have questions about the program or application, contact FLASH at (877) 221-7233 or email info@flash.org.
For business continuity and preparedness questions, please contact FEMA at FEMA-Private-Sector@fema.dhs.gov.
Signature Print Name Date

## Slide 54: Valuable Websites
America’s PrepareAthon! https://www.ready.gov/prepare
FLASH http://www.flash.org
National Hurricane Center http://www.nhc.noaa.gov/ https://noaanhc.wordpress.com/
Ready Floods https://www.ready.gov/floods
Ready Hurricanes https://www.ready.gov/hurricanes
Ready Business http://www.ready.gov/business

## Slide 55: APPENDIX A | Acronyms and Glossary
B | 
Backflow Valve | A valve designed to block drain pipes temporarily and prevent return flow.
Base Flood | Flood that has a one percent probability of being equaled or exceeded in any year.
Base Flood Elevations (BFE) | The computed elevation to which floodwater is anticipated to rise during the base flood. BFEs are shown on Flood Insurance Rate Maps (FIRMs) and on the flood profiles. The BFE is the regulatory requirement for the elevation or floodproofing of structures. The relationship between the BFE and a structure’s elevation determines the flood insurance premium.
C | 
Coastal Flooding | Flooding which occurs when water is driven onto land from an adjacent body of water. This generally occurs when there are significant storms, such as tropical and extratropical cyclones.
D | 
Debris | Materials carried by floodwaters, including objects of various size and suspended soils.
Design Flood Elevation (DFE) | Elevation of the highest flood, including freeboard, that a retrofitting method is intended to protect against.
Dry Floodproofing | Protecting a building by sealing its exterior walls to prevent the entry of floodwaters.
E | 
Elevation | In retrofitting, the process of raising a home or other building so that it is above the height of a given flood.
Evacuation Notice | If the danger is significant, state or local government officials may issue an evacuation notice. Evacuation orders may vary by state and community and range from voluntary to mandatory. When authorities issue a mandatory evacuation notice, leave the area immediately.
Extreme Wind Warning | An extreme wind warning is issued when extreme sustained winds of a major hurricane (115 mph or greater), usually associated with the eyewall, are expected to begin within an hour.

## Slide 56: APPENDIX A | Acronyms and Glossary
F | 
Flash Flood | A flood that rises and falls very quickly, usually characterized by high flow velocities.
Flood | Under the NFIP, “a general and temporary condition of partial or complete inundation of normally dry land areas” from 1) the overland flow of a lake, river, stream, ditch, etc.; 2) the unusual and rapid accumulation of runoff of surface waters; and 3) mudflows or the sudden collapse of shoreline land.
Floodproofing | Structural or nonstructural changes or adjustments included in the design, construction, or alteration of a building that reduce damage to the building and its contents from flooding and erosion.
Floodwall | Flood barrier constructed of manmade materials, such as concrete or masonry.
Freeboard | Additional amount of height included in the DFE to provide a factor of safety.
H | 
Hurricane | A hurricane is a tropical cyclone in which the maximum sustained surface wind (using the U.S. 1-minute average) is 74 mph or more. The term hurricane is used for Northern Hemisphere tropical cyclones east of the International Dateline to the Greenwich Meridian.
Hurricane Season | The portion of the year having a relatively high incidence of hurricanes. The hurricane season in the Atlantic, Caribbean, and Gulf of Mexico runs from June 1 to November 30.
Hurricane Warning | A hurricane warning is an announcement that sustained winds of 74 mph or higher are expected somewhere within the specified area in association with a tropical, subtropical, or post-tropical cyclone. Because hurricane preparedness activities become difficult once winds reach tropical storm force, the warning is issued 36 hours in advance of the anticipated onset of tropical-storm-force winds. The warning can remain in effect when dangerously high water or a combination of dangerously high water and waves continue, even though winds may be less than hurricane force.
Hurricane Watch | A hurricane watch is an announcement that sustained winds of 74 mph or higher are possible within the specified area in association with a tropical, subtropical, or post-tropical cyclone. Because hurricane preparedness activities become difficult once winds reach tropical storm force, the hurricane watch is issued 48 hours in advance of the anticipated onset of tropical storm force winds.
Hydrostatic Pressure | Force exerted on the walls and uplift (buoyancy) on floors by the floodwaters.

## Slide 57: APPENDIX A | Acronyms and Glossary
I | 
Inland Flooding | Any type of flooding that occurs that is not considered coastal flooding. For example flash floods, riverine floods, aerial flooding, etc.
L | 
Levee | Flood barrier constructed of compacted soil.
Lowest Floor | Floor of the lowest enclosed area within the building, including the basement. The only exception is an enclosed area below an elevated building, but only when the enclosed area is used solely for parking, building access, or storage and is compliant with relevant regulations.
M | 
Major Hurricane | A major hurricane is a hurricane which reaches Category 3 (sustained winds greater than 110 mph) on the Saffir/Simpson Hurricane Scale.
R | 
Retrofitting | Making changes to an existing home or other building to protect it from flooding or other hazards such as high winds and earthquakes.
S | 
Saffir-Simpson Hurricane Wind Scale | The Saffir-Simpson Hurricane Wind Scale is a 1 to 5 categorization based on the hurricane’s intensity at the indicated time. The scale provides examples of the type of damage and impacts in the United States associated with winds of the indicated intensity.
Service Equipment | The utility systems, heating and cooling systems, and large appliances in a retrofitted home.
T | 
Tropical Cyclone | A tropical cyclone is a warm-core non-frontal synoptic-scale cyclone, originating over tropical or subtropical waters, with organized deep convection and a closed surface wind circulation about a well-defined center. Once formed, a tropical cyclone is maintained by the extraction of heat energy from the ocean at high temperature and heat export at the low temperatures of the upper troposphere.

## Slide 58: APPENDIX A | Acronyms and Glossary
T | 
Tropical Depression | A tropical cyclone in which the maximum sustained surface wind speed (using the U.S. 1-minute average) is 38 mph or less.
Tropical Storm | A tropical storm is a tropical cyclone in which the maximum sustained surface wind speed (using the U.S. 1-minute average) ranges from 39 mph to 73 mph.
Tropical Storm Warning | A tropical storm warning is an announcement that sustained winds of 39 to 73 mph are expected somewhere within the specified area within 36 hours in association with a tropical, subtropical, or post-tropical cyclone.
Tropical Storm Watch | A tropical storm watch is an announcement that sustained winds of 39 to 73 mph are possible within the specified area within 48 hours in association with a tropical, subtropical, or post-tropical cyclone.
W | 
Wet Floodproofing | Protecting a building by allowing floodwaters to enter so that internal and external hydrostatic pressure are equalized. Usually, only enclosed areas used for parking, building access, or storage are wet floodproofed.

## Slide 59: APPENDIX B
PAGE # | TITLE OF DOCUMENT | LINK
2 | NOAA. Inland flooding: a hidden danger of tropical cyclones. June 25, 2012 | http://www.noaa.gov/stories/inland-flooding-hiddendanger-of-tropical-cyclones
5 | FEMA. Business Continuity Plan | www.fema.gov/media-library/assets/documents/89510
7 | FLASH email | info@flash.org
18 | FloodSmart | www.floodsmart.gov
25 | National Voluntary Organizations Active in Disaster | www.nvoad.org/volunteering
26 | FEMA. Business Continuity Plan | www.fema.gov/media-library/assets/documents/89510
26 | DRB Toolkit | www.drbtoolkit.org
26 | FEMA. Business Continuity Plan | www.fema.gov/media-library/assets/documents/89510
26 | Small Business Administration. Crisis Communication | http://www.agilityrecovery.com/assets/SBA/ crisiscomms.pdf
27 | FEMA. How to Prepare for a Hurricane. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98105
27 | FEMA Flood Map Service Center | https://msc.fema.gov/portal
28 | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98410
28 | Turn Around, Don’t Drown! | http://tadd.weather.gov/
28 | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98410
29 | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98410
29 | Insurance Coverage Discussion Form | http://www.fema.gov/media-library/assets/ documents/89528
29 | Emergency Supply List | http://www.fema.gov/media-library/assets/ documents/90354
30 | NOAA Weather Radio All Hazards | http://www.nws.noaa.gov/nwr/
30 | Be Smart. Take Part. Know Your Alerts and Warnings | http://www.community.fema.gov/action/access-alertsand-warnings
31 | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98410
31 | FEMA. How to Prepare for a Hurricane. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98105
32 | Remove Trees and Potential Windborne Missiles: Protecting Your Property from High Winds | http://www.fema.gov/media-library/assets/ documents/13270
The following is a list of websites and content referenced in this document.

## Slide 60: APPENDIX B
PAGE # | TITLE OF DOCUMENT | LINK
32 | FEMA P-936, Floodproofing Non-Residential Buildings | http://www.fema.gov/media-library/assets/ documents/34270
32 | FEMA P-259, Engineering Principles and Practices for Retrofitting Flood-Prone Residential Structures | http://www.fema.gov/media-library/assets/ documents/3001
33 | FEMA P-936, Floodproofing Non-Residential Buildings | http://www.fema.gov/media-library/assets/ documents/34270
33 | Emergency Response Plan | https://www.ready.gov/business/implementation/ emergency
34 | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds | https://www.fema.gov/media-library/assets/ documents/5264
34 | FEMA P-259, Engineering Principles and Practices for Retrofitting Flood-Prone Residential Structures | http://www.fema.gov/media-library/assets/ documents/3001
34 | FEMA P-936, Floodproofing Non-Residential Buildings | http://www.fema.gov/media-library/assets/ documents/34270 32 32
35 | FEMA. How to Prepare for a Hurricane. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98105
35 | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds | https://www.fema.gov/media-library/assets/ documents/5264
35 | Secure Built-Up and Single-Ply Roofs: Protecting Your Property from High Winds | https://www.fema.gov/media-library/assets/ documents/13270
36 | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Flood, and High Winds | https://www.fema.gov/media-library/assets/ documents/5264
36 | FEMA P-499, Home Builder’s Guide to Coastal Construction | http://www.fema.gov/media-library/assets/ documents/6131
36 | FEMA P-499, Home Builder’s Guide to Coastal Construction | http://www.fema.gov/media-library/assets/ documents/6131
37 | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Flood, and High Winds | https://www.fema.gov/media-library/assets/ documents/5264
37 | FEMA P-499, Home Builder’s Guide to Coastal Construction | http://www.fema.gov/media-library/assets/ documents/6131
37 | Secure Metal Siding and Metal Roofs: Protecting Your Property from High Winds | https://www.fema.gov/media-library/assets/ documents/13270
37 | Maintain EIFS Walls: Protecting Your Property from High Winds | https://www.fema.gov/media-library/assets/ documents/13270
38 | Reinforce or Replace Garage Doors: Protecting Your Property from High Winds | https://www.fema.gov/media-library/assets/ documents/13270
The following is a list of websites and content referenced in this document.

## Slide 61: APPENDIX B
PAGE # | TITLE OF DOCUMENT | LINK
38 | Protect Windows and Doors with Covers: Protecting Your Property from High Winds | https://www.fema.gov/media-library/assets/ documents/13270
38 | FEMA P-499, Home Builder’s Guide to Coastal Construction | http://www.fema.gov/media-library/assets/ documents/6131
38 | FEMA P-424, Design Guide for Improving School Safety in Earthquakes, Floods, and High Winds | https://www.fema.gov/media-library/assets/ documents/5264
39 | FEMA P-804, Wind Retrofit Guide for Residential Buildings | https://www.fema.gov/media-library/assets/ documents/21082
39 | FEMA P-361, Safe Rooms for Tornadoes and Hurricanes: Guidance for Community and Residential Safe Rooms | https://www.fema.gov/media-library/assets/ documents/3140
39 | FEMA P-320, Taking Shelter from the Storm: Building a Safe Room for Your Home or Small Business | https://www.fema.gov/fema-p-320-taking-shelterstorm-building-safe-room-your-home-or-smallbusiness
39 | ICC/NSSA 500-2014: Standard for the Design and Construction of Storm Shelters | http://shop.iccsafe.org/icc-500-2014-icc-nssastandard-for-the-design-and-construction-of-stormshelters-1.html
40 | Quick Guide Flood Hazard Elevation and Siting Criteria for Community Safe Rooms | http://www.fema.gov/media-library/assets/ documents/101965
40 | FEMA P-431, Tornado Protection: Selecting Refuge Area in Buildings | https://www.fema.gov/media-library/assets/ documents/2246
40 | FEMA P-550, Recommended Residential Construction for Coastal Areas: Building on Strong and Safe Foundations | http://www.fema.gov/es/media-library/assets/ documents/3972
40 | FEMA P-312, Homeowner’s Guide to Retrofitting | http://www.fema.gov/media-library/assets/ documents/480
40 | FEMA P-936, Floodproofing Non-Residential Buildings | http://www.fema.gov/media-library/assets/ documents/34270
40 | FEMA P-259, Engineering Principles and Practices for Retrofitting Flood-Prone Residential Structures | http://www.fema.gov/media-library/assets/ documents/3001
41 | FEMA P-936, Floodproofing Non-Residential Buildings | http://www.fema.gov/media-library/assets/ documents/34270
41 | FEMA P-259, Engineering Principles and Practices of Retrofitting Flood-Prone Residential Structures | http://www.fema.gov/media-library/assets/ documents/3001
42 | Emergency Management Agencies | http://www.fema.gov/emergency-managementagencies
42 | FEMA. Prepare Your Organization for a Hurricane Playbook. America’s PrepareAthon! | http://www.fema.gov/media-library/assets/ documents/98410
The following is a list of websites and content referenced in this document.

## Slide 62: APPENDIX B
PAGE # | TITLE OF DOCUMENT | LINK
53 | FLASH email | info@flash.org
53 | FEMA Private Sector Division Email | FEMA-Private-Sector@fema.dhs.gov
54 | America’s PrepareAthon! | https://ready.gov/prepare
54 | FLASH | http://www.flash.org
54 | National Hurricane Center | http://www.nhc.noaa.gov/ https://noaanhc.wordpress.com/
54 | Ready Floods | https://www.ready.gov/floods
54 | Ready Hurricanes | https://www.ready.gov/hurricanes
54 | https://www.ready.gov/business | https://www.ready.gov/business
55 | FEMA. Install Sewer Backflow Valves | http://www.fema.gov/media-librarydata/20130726-1627-20490-2015/how2007_ sewer_4_11.pdf
55 | National Weather Service. Glossary | http://www.nws.noaa.gov/glossary/
56 | National Weather Service. Glossary | http://www.nws.noaa.gov/glossary/
57 | National Weather Service. Glossary | http://www.nws.noaa.gov/glossary/
58 | National Weather Service. Glossary | http://www.nws.noaa.gov/glossary/
The following is a list of websites and content referenced in this document.